## Slide 1: Iso-Surface Extraction

## Slide 2: Iso Surface
Iso surface (aka implicit surface) is defined as f(x,y,z)=0.
Polygonal mesh, and CAD surface is explicitly defined.

## Slide 3: Iso Surface vs. Explicit Surface
Iso Surface
  Advantages:
    If f(x,y,z) is a continuous function, it always defines a valid closed solid.
    No numerical instability when merging multiple solid bodies.
  Disadvantages
    The iso surface itself is not useful until it is converted to an explicit surface.
Explicit Surface
  Advantages:
    Can be rendered.
    Easier manipulation.
  Disadvantages:
    Suffer from numerical instability.
    May fail to define a valid closed solid.

## Slide 4: Iso Surface Extraction
Iso surface itself is not useful.
Need to extract, or convert to an explicit surface.
Common method is to define the implicit function f(x,y,z) over a structured grid, and then connect zeros to make it a polygonal mesh.

## Slide 5: Iso Curve Extraction over a 2D grid
f(x,y)>0
f(x,y)<0
Iso curve

## Slide 6: Iso Surface Extraction over a 3D grid
(1) Make iso-lines over the rectangular faces

## Slide 7: Iso Surface Extraction over a 3D grid
(2) Then connect them to form a loop(s)

## Slide 8: Iso Surface Extraction over a 3D grid
(3) Finally tessellate into triangles.

## Slide 9: Our Problem
Want to make a smoothly connected lattice structure using a iso-surface method called Metaball.
We first create a mesh, and then thicken edges of the mesh.

## Slide 10: Need to cut off outside volume.

## Slide 11: Cutting off the Outside Volume
In other words, we want to take an intersection of the implicit functions.
At this time, it creates a very jaggy edges where the boundary of the input mesh and the implicit surface meet.
We want to explore the possibility of taking intersection of two implicit functions without creating jaggy edges.

## Slide 12: If I want to take an intersection....
f(x,y)>0
f(x,y)<0
Iso curve
Another implicit function:
g(x,y)=1 inside, g(x,y)=-ε outside, where ε is a very small positive number.

## Slide 13: By simply taking f'=f*g, this is what we get.
f'(x,y)>0
f'(x,y)<0
Iso curve
f'(x,y)=-ε

## Slide 14: This is what we want.
f(x,y)>0
f(x,y)<0
Iso curve
Another implicit function:
g(x,y)=1 inside, g(x,y)=-ε outside, where ε is a very small positive number.
We may want an additional freedom inside the grid cell.

## Slide 15: Where to start:
Read the original paper of the Metaball method []
Write a code for 2D iso-curve extraction.
  You can define a function like f(x,y)=x2+y2-1, and draw a curve defined by f(x,y)=0.
  By the way, I wanted to make it an assignment for 24783, but turned out someone else was doing the same in another MechE course, and I had to ditch the idea :-P